## Slide 1: Smart In-situ Visualization for Large-scale Numerical Simulations Aiming at Efficient Knowledge Acquisition
Naohisa Sakamoto naohisa.sakamoto@people.kobe-u.ac.jp
Kobe University Kobe, Japan
The 4th China-Japan Joint Visualization Workshop July 24, Wuhan, China (Online)

## Slide 2: In-situ processing
Visualization and analysis become more challenging task for large-scale data generated from faster and powerful supercomputers.
RIKEN Center for Computational Science (R-CCS)
  K computer was decommissioned after several years.
  Fugaku system is underway
    consist of more than 150,000 processing nodes
    expected to deliver even larger volume of simulation results
K computer (SPARC)
Fugaku Supercomputer
(ARM-based CPU)
OpenStack-based
Private Cloud
(x86/GPU)
Local FS
In
Out
“Staging”
Login Server
(x86)
Global FS
Post-hoc
In-situ

## Slide 3: In-situ visualization
Pre-defined visualization parameters
  File staging based in-situ processing
  Large number of output images
Post-analysis with large image database
  Difficult to find the important features related to the correct understanding of the underlying physical phenomena

## Slide 4: Our approach
In-situ timestep selection
  Based on the amount of change between the simulation timesteps
  Helpful for the data I/O and visualization cost savings
Simulation
Visualization
Storage
In-Situ Timestep Selection
. . .
. . .

## Slide 5: Proposed method
Adaptive timestep selection for in-situ visualization
  Spatio-temporal variations between volumes
  Adaptive timestep sampling
Vt-1
Vt
‥ ‥
‥ ‥
Variations
Time
Not vis
Vis
Not important
Important

## Slide 6: Spatio-temporal variations
Time-varying simulations
Time
V0
V1
0
1
t
Vt
‥ ‥
‥ ‥
Vt = {Vt1,Vt2, … , Vtm, …, VtM}
‥‥
‥‥
Vt1
Vt2
Vtm
Vtm-1
Vtm+1

## Slide 7: Spatio-temporal variations
Probability density function P of each subvolume
  Kernel Density Estimation (KDE)
‥‥
‥‥
Vt1
Vt2
Vtm
Vtm-1
Vtm+1
Ptm
S
‥‥
P
: position
: scalar data
: number of scalar data
: bandwidth
: Gaussian basis function

## Slide 8: Spatio-temporal variations
Relative divergence D between PDFs
  Kullback-Leibler (KL) divergence
Vt-ΔT
t-ΔT
t
Vt
Time
‥‥
Pt-ΔT
m
Ptm
‥‥
: time interval used for calculating the divergence
Dtm

## Slide 9: Spatio-temporal variations
Relative divergence D between PDFs
  Kullback-Leibler (KL) divergence
Time
D
t - ΔT
t
Dt = max(Dt1, Dt2, … , Dtm, …, DtM)
‥‥
‥‥
Dt1
Dt2
Dtm
Dtm-1
Dtm+1

## Slide 10: Adaptive time sampling
Variation patterns
D
THR
A
B
C
A
t0
t1
t2
‥‥
t’k
t’k+1
t’k-1
‥‥
‥‥
Δt
Δt’
ΔT
Tp-1
Tp
Tp+1
Time

## Slide 11: Visualization interval
Granularity R for low variation region
Δt
Δt’
ΔT
Tp-1
Tp
Time
R = 1
Stacking
Rendering
R = 2
R = 4
Fine
Coarse
Visualization Interval
Time interval of data output
from simulation
Time interval of KL divergence calculation

## Slide 12: Visualization interval
Granularity for each pattern
  Pattern A
    Coarse sampling
    Using specified R
  Pattern B
    Fine sampling
    Using R = 1
  Pattern C
    Combined sampling
    Using R = 1 (fine) in the first half and specified R in the other half
A
B
C
Coarse
(Specified R)
Fine
(R = 1)
Coarse
(Specified R)
Fine
(R = 1)

## Slide 13: Experiment
Numerical simulation of sibilant fricatives
  Implicit compressible flow solver based on OpenFOAM
  Unstructured volumes
    3,197,279 hexahedrons
    48 subvolumes
    20,000 timesteps

## Slide 14: Experiment
Environment
  K pre-post cloud system
    X86 based on-premise could system
    Dual Intel Xeon Platinum 8168 (Skylake) 24cores/2.7GHz
    48 vCPUs on the VM for the evaluation
Software
  Simulation: OpenFOAM
  Visualization: KVS (original toolkit)
  Parallel rendering: 234 image compositor

## Slide 15: Result
Changes of KL divergence (D)
  Simulation timesteps: 20,000
  KL divergence calculation interval (ΔT): 100
    Number of simulations (a): 5
    Number of stacking data (b): 20
Time step
KL divergence

## Slide 16: Result
Number of vis. images and reduction ratio
  Total number of stacked data: 4,000
THR | R=5 | R=10
0 | 4,000 (0%) | 4,000 (0%)
0.01 | 3,452 (13.7%) | 3,384 (15.4%)
0.02 | 3,100 (22.5%) | 2,896 (21.6%)
0.03 | 2,856 (28.6%) | 2,616 (34.6%)
0.04 | 2,496 (37.6%) | 2,288 (42.8%)
0.05 | 2,064 (48.4%) | 1,892 (52.7%)
THR: Threshold for the KL divergence (D)
R: Granularity for the time sampling for A and C interval patterns

## Slide 17: Result
In-situ visualization results with and without our method
  THR = 0.005
Original
(4,000 images)
Our method with R=5
(2,064 images)
Our method with R=10
(1,892 images)

## Slide 18: Conclusion
Adaptive timestep control for in-situ visualization
  Spatio-temporal variations between the simulation results based on the Kullback-Leibler divergence
  Adaptive timestep control in consideration of the variation changing patterns
  Utilizing adaptive timestep sampling mechanism for reducing the amount of data for the subsequent processing (e.g. data storing for the post-hoc visualization and analytics, in-situ/in-transit visualization)
Future works
  Optimal parameter selection for the input time intervals
  Viewpoint selection without missing significant physical phenomenon